## Slide 1
STK Shield Plus – Overbraid
Prepared by:
Jason DiMartino – Scientist II
Kevin-Druis Merenda – Principal Scientist I and Lead Product Manager

## Slide 2
Demo Background

## Slide 3: Demo Background
EMA’s overbraid workflow in STK Shield is designed to evaluate transients coupled onto a cable conductor from an applied EM pulse, based on the shielding effectiveness of the cable harness
It can be important to quantify these transients when cable ends are connected to sensitive electronics/avionics

## Slide 4
Setting up the STK Scenario

## Slide 5: Setting up the STK Scenario
Open the provided STK .sc Scenario within the demo folder to retrieve a preset Scenario with a preset Aircraft, Ground Vehicle, Place, Satellite, and Target
For this demo we will use Place1
The other objects are used in the other STK Shield Plus demos, and should be unchecked here

## Slide 6
Setting up Overbraid Options

## Slide 7: Setting up Overbraid options
Click the Surface Charging Options item in the EMA toolbar on the right.
Graph Object: Place/Place 1
Cable Length: 3.3
Termination Resistance 1: 1E-06
Termination Resistance 2: 50
Alpha: 1.929E+19
Amplitude: 1239
Time to Peak: @.104E-09
Direction: +Y – any direction but –Z works here
Headless: False – if headless, will run without opening the Shield Plus GUI, reducing some computational overhead
Click Run Workflow to open the Discovery UI and run the solver.

## Slide 8: Overbraid Options

## Slide 9: Overbraid Options
The workflow opens a default workflow geometry in STK Shield, creating a cable, assigning materials, and applying the designated EM pulse
The model can then be modified, and changes will apply to subsequent runs of the workflow
  For more in-depth Shield Plus tutorials, please see the help button in the ‘Other’ section of the Shield Plus ribbon
Tip: Launch Shield Plus
without running a sim

## Slide 10: Overbraid Options
To alter the response on this cable, the following can be changed in the STK options:
  The Simulated load at the end of the cable can be changed by adjusting the termination resistance
  The length of the cable can be increased/decreased, resulting in changes in coupling at specific frequencies
  The direction of propagation of the incoming wave can be changed to simulate a difference orientation of the cable relative to the source
  Properties of the default Gaussian pulse can be modified to account for changes in source bandwidth and magnitude of the pulse

## Slide 11: Default Model
The workflow automatically creates a sample cable workbench with the elements & orientation shown.
The conductive ground plane will block excitation from the –Z direction, so choose a different option when initializing the workflow.

## Slide 12
Analyzing Results

## Slide 13: Analyzing Results

## Slide 14: Analyzing Results
Once the simulation has completed, conductor and shield transients can be plotted from the results in the Discovery tree, and will also appear in STK
In this demo, default probes capture voltage and current at both ends of the cable shield and conductor